## Slide 1: SHORT-TERM ELECTRICAL LOAD FORECASTING FOR BANESHWOR FEEDER USING MACHINE AND DEEP LEARNING MODELS
Presenter,
Sujit Koirala
The Department Of Electrical Engineering
Masters Of Science In Power System Engineering
Tribhuvan University
Institute of Engineering
Pulchowk Campus

## Slide 2: Table of contents 01 05 04 02 03
Introduction
Literature Review
Methodology
Problem Statement
Objectives
Conclusion
06
Future Work
07

## Slide 3: Introduction 01
Short-term electrical load forecasting is essential for planning and operating a reliable power system. It helps utilities manage demand, reduce costs, and improve overall efficiency. The Baneshwor Feeder serves a mix of households, businesses, and small industries, and its load pattern shifts with time, weather, and community activities. This project explores how modern machine learning and deep learning models can forecast its hourly demand more accurately than traditional methods.
Fig 1.1: Baneshwor Feeder View
Slide 1 - 12/18/2025

## Slide 4
Fig 1.2: Substation & Transmission Line Network Baneshwor

## Slide 5: Problem Statement
Existing forecasting methods for the Baneshwor Feeder rely on manual estimates or traditional statistical models that struggle to capture nonlinear and rapidly changing load patterns.
Weather changes, calendar effects, and local demand variations make the load behavior more complex, reducing the accuracy of current forecasting practices.
Inaccurate forecasts lead to poor generation scheduling, higher operational costs, increased technical losses, and potential reliability issues in the distribution system.
There is no systematic study that applies and compares advanced machine learning and deep learning models for short-term forecasting of this specific feeder.
02
Slide 2 - 12/18/2025

## Slide 6: Objectives
To develop an accurate short-term electrical load forecasting model for the Baneshwor Feeder by integrating cleaned load data, weather variables, and advanced ML/DL techniques.
Main Objective
03
Slide 3 - 12/18/2025
To collect, clean, and standardize multi-year feeder load and weather data
To engineer meaningful temporal and weather-based features for forecasting
To compare the performance of ML models (LR, Ridge, SVR, RF, GBR, XGBoost)
To evaluate deep learning models (MLP, LSTM, GRU) using sequential forecasting methods
To identify the best-performing model based on RMSE, MAE, MAPE, and R²
To visualize load behavior across daily, weekly, and seasonal patterns
To prepare a final forecasting framework suitable for real-world feeder operations
Specific Objective

## Slide 7: Literature Review
04
Slide 5 - 12/18/2025
S.N. | Author(s) & Year | Models Used | Input Features | Dataset / Study Area | Key Findings | Research Contribution
1 | Singla et al. (2019) | ANN | Dew point, dry bulb temperature, humidity | Power system dataset | ANN effectively captured nonlinear relation between weather and load | Demonstrated ANN suitability for STLF
2 | Desai et al. (2021) | Prophet (Meta) | Time, temperature, humidity, weather forecast | Electrical load data | Prophet handled seasonality and missing data efficiently | Introduced statistical ML hybrid for STLF
3 | Matrenin et al. (2022) | XGBoost, AdaBoost, RF, SVR, DT | Historical load data | Isolated power systems | Gradient boosting models outperformed traditional ML | Highlighted superiority of ensemble boosting
4 | Aguilar Madrid & Antonio (2021) | RF, SVR, XGBoost | Load history, weather, holidays | Regional power system | XGBoost achieved highest accuracy | Justified tree-based ensemble models
5 | Guo et al. (2021) | SVM, RF, LSTM, Ensemble | Load and weather features | Large-scale power system | Fusion of ML and DL improved accuracy | Motivated ensemble forecasting strategies

## Slide 8: Literature Review
04
Slide 4 - 12/18/2025
S.N. | Author(s) & Year | Models Used | Input Features | Dataset / Study Area | Key Findings | Research Contribution
6 | Saglam et al. (2024) | ANN, SVR + PSO, DO, GRO | Load, GDP indicators | Power system dataset | ANN + Growth Optimizer performed best | Linked optimization techniques with ML
7 | Jain & Gupta (2024) | SVM, LSTM, RNN, Ensembles | Preprocessed load data | Electrical grid dataset | Ensemble and DL models outperformed statistical methods | Emphasized preprocessing and feature selection
8 | Chapagain et al. (2021) | ML, DL (LSTM) | Load history, temperature, day type | Kathmandu Valley, Nepal | LSTM showed lowest MAPE and RMSE | Nepal-based validation of DL models
9 | Acharya et al. (n.d.) | RNN | Historical load features | Gothatar Feeder, Nepal | RNN outperformed exponential smoothing methods | Feeder-level DL forecasting in Nepal
10 | Cordeiro-Costas et al. (2023) | RF, SVR, XGBoost, MLP, LSTM, Conv-1D | Load and weather data | Power system dataset | LSTM achieved lowest forecasting error | Compared CNN and RNN architectures

## Slide 9: Methodology
Data
Acquisition
Data
Preprocessing
Exploratory
Data Analysis
01
02
03
Model Development
04
Model Training
& Validation
06
Performance Evaluation
07
05
Slide 6 - 12/18/2025
Collect raw load and weather data
Clean, align, and standardize all data
Understand patterns, trends, correlations
Design ML/DL forecasting models
Train models and tune parameters
Compare models using error metrics

## Slide 10: Data Acquisition & Preprocessing
5.1
Load Data: Hourly MW readings from Baneshwor Feeder.
Weather Data: Temperature, Humidity, and Rainfall.
Challenges: Missing Value, Nepali (BS) Date Format, Outliers
Standardization: Converted all timestamps to Gregorian (AD).
Cleaning: Handled missing values via Forward/Backward fill; detected outliers using IQR.
Feature Engineering: Created Hour, Day, Month and Time Features from time.
Slide 7 - 12/18/2025

## Slide 11: Data Acquisition & Preprocessing
5.1
Time | Power (MV) | Air Temperature (°C) | Global Solar Radiation (W/) | Relative Humidity (%)
2022-10-19 01:00 | 0.8 | 14.5 | 0 | 88.8
2022-10-19 02:00 | 0.8 | 14.4 | 0 | 87.9
2022-10-19 03:00 | 0.8 | 14 | 0 | 92.3
2022-10-19 04:00 | 0.8 | 13.2 | 0 | 95.8
2022-10-19 05:00 | 0.8 | 12.65 | 0 | 97.9
2022-10-19 06:00 | 1.2 | 12.1 | 0 | 100
2022-10-19 07:00 | 2 | 12 | 18.6 | 100
2022-10-19 08:00 | 2.3 | 14.3 | 171.3 | 92.9
2022-10-19 09:00 | 2.1 | 17.2 | 393.6 | 77
Time | Power (MV) | Air Temperature (°C) |  | Relative Humidity (%)
2022-10-19 01:00 | 0.8 | 14.5 | 0 | 88.8
2022-10-19 02:00 | 0.8 | 14.4 | 0 | 87.9
2022-10-19 03:00 | 0.8 | 14 | 0 | 92.3
2022-10-19 04:00 | 0.8 | 13.2 | 0 | 95.8
2022-10-19 05:00 | 0.8 | 12.65 | 0 | 97.9
2022-10-19 06:00 | 1.2 | 12.1 | 0 | 100
2022-10-19 07:00 | 2 | 12 | 18.6 | 100
2022-10-19 08:00 | 2.3 | 14.3 | 171.3 | 92.9
2022-10-19 09:00 | 2.1 | 17.2 | 393.6 | 77
Table 4.1 Finalized Sample Dataset
Slide 8 - 12/18/2025

## Slide 12: Exploratory Data Analysis
5.2
Fig 4.2 Average Load by House of Day and Load Distribution by Hour
Slide 9 - 12/18/2025
These graphs show that the average load increases from 8 am in morning and peaks around 7 pm at night and then decreases from then.
The box plot shows the high and low power usage outside normal range (Outliers)

## Slide 13: Exploratory Data Analysis
5.2
Fig 4.3 Feature Relationship and Average Load by Month
Slide 10 - 12/18/2025
Temperature and Humidity show a clear influence on energy spikes, solar radiation levels have a less direct impact on the overall load.

## Slide 14: Exploratory Data Analysis
5.2
Fig 4.3 Feature Relationship and Average Load by Month
Slide 10 - 12/18/2025
The load around the 1st Month and 12th month are the highest and the lowest is 3rd and 4th.

## Slide 15: Exploratory Data Analysis
5.2
Fig 4.4 Correlation Matrix
Slide 11 - 12/18/2025
This correlation matrix shows how different all the columns in the data are related to reach other.

## Slide 16
LSTM (Long Short-Term Memory)
GRU (Gated Recurrent Unit )
MLP (Multilayer Perceptron)
XGboost
Random Forest
Gradient Boosting
SVR (Support Vector Regression)
Ridge Regression
Linear Regression
Machine Learning Models
Deep Learning Model
Model Development & Training
5.3
Slide 12 - 12/18/2025

## Slide 17
Performance Evaluation
5.4
Machine Learning Models
Fig 4.5 Machine Learning Models Evaluation Results
Slide 13 - 12/18/2025
Tuned XGBoost is the most accurate performer with the lowest error rates (MAE of 0.2570 and RMSE of 0.3840).

## Slide 18
Performance Evaluation
5.4
Machine Learning Models
Fig 4.5 Machine Learning Models Evaluation Results
Slide 13 - 12/18/2025
Tuned XGBoost is the clear winner, achieving the highest accuracy ( of 0.8312) and the lowest average error rate (12.69%).
These charts compare different machine learning models to see which one best predicts energy demand. Tuned XGBoost is the clear winner, achieving the highest accuracy ($R^2$ of 0.8312) and the lowest average error rate (12.69%).

## Slide 19
Performance Evaluation
5.4
Machine Learning Models
Fig 4.6 Machine Learning Models Actual vs Predicted Load
Slide 14 - 12/18/2025
The two top-performing machine learning models, Random Forest and XGBoost, predict actual energy load over time.

## Slide 20
Performance Evaluation
5.4
Deep Learning Models
Fig 4.7 Deep Learning Models Evaluation Results
Slide 16 - 12/18/2025
The MAE of LSTM model has the lowest average prediction error. The RMSE values are almost the same for all three models, meaning they make similar errors. Overall, LSTM gives the most accurate and consistent predictions.

## Slide 21
Performance Evaluation
5.4
Deep Learning Models
Fig 4.7 Deep Learning Models Evaluation Results
Slide 16 - 12/18/2025
The R² graph shows that the LSTM model achieves the highest explanatory power. The MAPE results indicate that GRU yields the lowest prediction error.

## Slide 22
Performance Evaluation
5.4
Deep Learning Models
Fig 4.7 LSTM Model Sample Forecast vs Actual
Slide 17 - 12/18/2025
Load (MV)
This graph compares real-world electricity usage (Actual) against an LSTM model's predictions over a 24-hour period

## Slide 23
Performance Evaluation
5.4
Rank | Model | MAE | RMSE | R² | Category
1 | XGBoost (Tuned) | 0.257 | 0.384 | 0.8312 | ML
2 | Random Forest (Tuned) | 0.293 | 0.435 | 0.7831 | ML
3 | Random Forest | 0.305 | 0.444 | 0.7739 | ML
4 | XGBoost | 0.313 | 0.448 | 0.7693 | ML
5 | Gradient Boosting | 0.330 | 0.468 | 0.7486 | ML
6 | SVR | 0.318 | 0.483 | 0.7324 | ML
7 | Ridge Regression | 0.502 | 0.648 | 0.5182 | ML
8 | Linear Regression | 0.502 | 0.648 | 0.5182 | ML
9 | LSTM | 0.467 | 0.498 | 0.014 | DL
10 | GRU | 0.482 | 0.499 | 0.012 | DL
11 | MLP | 0.618 | 0.499 | 0.011 | DL
Over All Model Ranking
Table 4.2 ML and DL over all Models Ranking
Slide 20 - 12/18/2025

## Slide 24: Conclusion
The study successfully developed and evaluated ML and DL models for short-term load forecasting of the Baneshwor Feeder.
Ensemble ML models particularly XGBoost (Tuned) achieved the highest forecasting accuracy across all evaluation metrics.
Deep learning models (LSTM, GRU, MLP) underperformed due to limited dataset size and weaker temporal patterns.
Feature engineering, especially time-based and cyclical features, significantly improved ML performance.
The final recommended model for practical deployment is XGBoost (Tuned) due to its high accuracy, robustness, and operational efficiency.
6
Slide 21 - 12/18/2025

## Slide 25: Future Work
7
Slide 21 - 12/18/2025
The proposed forecasting framework can be extended to multiple feeders beyond the Baneshwor feeder to evaluate its scalability and wider applicability.
While this study focuses on short-term load forecasting, future work can explore medium- and long-term load prediction for better planning and decision-making.
The model performance can be further improved by using a longer historical dataset covering more years of load and weather data.

## Slide 26
Thanks!
Do you have any questions?
Presenter,
Sujit Koirala
The Department Of Electrical Engineering
Masters Of Science In Power System Engineering
Tribhuvan University
Institute of Engineering
Pulchowk Campus

## Slide 27: References
Acharya, S., Luintel, M. C., & Badrudoza, M. (n.d.). Short-term load forecasting of Gothatar feeder of Nepal Electricity Authority using Recurrent Neural Network. Publisher not specified.
Desai, S., Dalal, T., Kadam, S., & Mishra, S. (2021). Electrical load forecasting using machine learning. IEEE (ICSCAN 2021).
Singla, M. K., Gupta, J., Nijhawan, P., & Oberoi, A. S. (2019). Electrical load forecasting using machine learning. International Journal.
Saglam, M., Lv, X., Spataru, C., & Karaman, O. A. (2024). Instantaneous electricity peak load forecasting using optimization and machine learning. Energies.
Matrenin, P., Safaraliev, M., Dmitriev, S., Kokin, S., Ghulomzoda, A., & Mitrofanov, S. (2022). Medium-term load forecasting in isolated power systems based on ensemble machine learning models. Energy Reports.
Aguilar Madrid, E., & Antonio, N. (2021). Short-term electricity load forecasting with machine learning. Information.
Cordeiro-Costas, M., Villanueva, D., Eguía-Oller, P., Martínez-Comesaña, M., & Ramos, S. (2023). Load forecasting with machine learning and deep learning methods. Applied Sciences.
Guo, W., Che, L., Shahidehpour, M., & Wan, X. (2021). Machine-learning-based methods in short-term load forecasting. The Electricity Journal.
Chapagain, K., Acharya, S., Bhusal, H., Katuwal, S., Lakhey, O., Neupane, P., Sah, R. K., Tamang, B., & Rajbhandari, Y. (2021). Short-term electricity demand forecasting for Kathmandu Valley, Nepal. Kathmandu University Journal of Science, Engineering and Technology.